## Slide 1: SMART INDIA HACKATHON 2026
JalRakshak
Problem Statement ID - SIH26255
Problem Statement Title - Development of a solution using AI and ML to monitor the functionality of FHTC in real time at both the Gram Panchayat and household levels. This solution should provide alerts on water quality issues, allow village members to give feedback through mobile devices, and automatically sync data with IMIS/Sujal Gaon IDs.
Organization - Ministry of Jal Shakti (MoJS)
Department - National Jal Jeevan Mission (NJJM), Department of Drinking Water & Sanitation (DDWS)
Theme - Clean & Green Technology
PS Category - Hardware
Team ID - [enter from portal]
Team Name - Team Vistaar
Your Water. Your Village. Your Voice.

## Slide 2: THE PROBLEM & OUR SOLUTION
Team Vistaar
THE PROBLEM
Found out too late
Problems surface through periodic reports and field inspections, by which time a tap may be dry for days
Disruptions nobody sees
Non-functional taps, intermittent supply, poor water quality, low pressure and failing pipes show up only when someone complains
Villagers have no easy voice
No quick way to report a dry tap, share a photo, or confirm that the water really came back
Data sits in separate places
Sensors, mobile apps, water-quality results and citizen feedback are never seen together
A tap is not a service
98.1% of surveyed homes had a tap, yet only 76.0% were assessed as functional [1]
OUR SOLUTION: JALRAKSHAK
1
Continuous FHTC monitoring
at Gram Panchayat and household level, using AI/ML
2
Real-time alerts
for supply disruption, water quality deterioration, low pressure, leakages and infrastructure failure
3
Villagers speak up
feedback, complaints, photographs and geo-tagged observations from a phone, in local languages
4
Early detection and prediction
AI/ML spots abnormal service patterns early, predicts failures and ranks maintenance
5
Automatic sync
monitoring data, alerts and feedback flow to IMIS, Sujal Gaon IDs and other JJM platforms
6
Dashboards for every level
GIS maps, service status indicators and analytics from VWSC to State
7
Built to grow
scalable, interoperable, secure and easy to deploy
SENSE
Nodes + villagers
UNDERSTAND
Rules + AI/ML
ALERT
Alert Center
REPORT
IMIS / JJM platforms
FIX
Task + repair
VERIFY
Readings recover
DEMO VIDEO (YouTube)
[add link after upload]
For: Village Water & Sanitation Committees (VWSCs), Gram Panchayats, implementing agencies and State authorities.
[1] DDWS, Functionality Assessment of Household Tap Connection, National Report 2024 (weighted sample estimates).

## Slide 3: TECHNICAL APPROACH
Team Vistaar
Hardware we use and how it connects (circuit diagram on the next slide)
ESP32 node
Reads sensors through ADC, I2C and GPIO; sleeps between samples
LoRa SX1276
SPI radio, 865-867 MHz, node to village gateway
Pi gateway
Buffers readings, sends over 4G MQTT to the ingestion API
Acoustic sensor
Piezo clamp on the pipe; leak noise is amplified, filtered and analysed on the node
Chlorine sensor
4-20 mA probe in a flow cell at the tail end; measured mg/L, low-chlorine alert
Pressure x2
4-20 mA transmitters, head and tail; low-pressure alert
Flow meter x2
Pulse output, head and tail; head-to-tail gap means a leak
Ultrasonic level
JSN-SR04T on the tank; supply and tank health
Solar + battery
12 V 10 W panel, 7 Ah battery, IP65 box; buck and boost rails

## Slide 4: FEASIBILITY AND VIABILITY
Team Vistaar
Circuit of sensor node B (pipeline head / tail): ESP32 with LoRa, ADS1115, 4-20 mA loops, flow, acoustic and tank-level inputs.
Scalability
One village, then a cluster per gateway, block, district, state
Stateless APIs; PostgreSQL + PostGIS
Same node design in every village
Interoperability
Keyed to Sujal Gaon and Sujalam Bharat IDs
Sync with IMIS, JJM Dashboard, WQMIS
Open formats: REST/OpenAPI, GeoJSON, CSV
Data security
Role-based access by village; hashed passwords
Rate limits, audit log, GPS removed from photos
No personal data sent to other platforms
Ease of deployment
Solar node, plug-in LoRa gateway, no grid cabling
Mobile web app: nothing to install
Docker deployment, one configuration file
Node installation concept
Solar-powered pole node with an IP65 box
Clamp-on acoustic sensor: no digging
Chlorine flow cell at the tail end
LoRa to the Panchayat gateway
Feasibility analysis
Off-the-shelf sensors, ESP32, LoRa, Raspberry Pi
Node firmware and gateway written; 278 automated tests pass
Open-source software; rules work from day one, AI/ML improves with data
Potential challenges and strategies to overcome them
False alarms: persistence windows; HIGH needs two kinds of evidence
Sensor fault or drift: health gate; chlorine probe checked with a DPD kit
Rural network: gateway buffers readings, sends when online
Trust in AI: every score shows its reasons
Leak vs noise: per-pipe acoustic baseline plus flow gap
Platform access: adapters ready; official access and specifications needed

## Slide 5: IMPACT AND BENEFITS
Team Vistaar
USERS INVOLVED
Villagers
Report problems with a photo, check their tap daily, and get alerts and advisories in their own language
VWSC and Gram Panchayat
See alerts, household tap status and a ranked repair list; confirm that water is really restored
Technicians and operators
Receive tasks with the pipeline, evidence and location; close them when readings recover
Implementing agencies
Plan preventive maintenance from risk and failure windows instead of waiting for breakdowns
District and State authorities
Multi-level analytics and GIS; data flows to IMIS, Sujal Gaon IDs and the JJM platforms
SOCIAL BENEFITS
Dry taps get fixed sooner, and the villager is told when water is restored
A voice for every household, in local languages
Boil-water advisories reach homes when a test fails
Tail-end homes stop being invisible
ECONOMIC BENEFITS
Inspect the riskiest pipes first: fewer repeat repairs and wasted visits
Small leaks are fixed before they become bursts
Less treated water lost to unseen leaks
Evidence replaces guesswork in planning and budgets
ENVIRONMENTAL BENEFITS
Early leak detection saves treated water and pumping energy
Solar-powered nodes: no grid cabling
Low-power LoRa links and sleep cycles
Measured chlorine helps avoid both under- and over-dosing
EARLY DETECTION AND PREDICTION, THEN ACTION
DETECT EARLY
Acoustic leak noise, pressure trend, chlorine probe and sensor health, before villagers notice
PREDICT
Pressure forecast, chlorine outlook and each pipeline's failure window, with reasons
ACT BEFORE IT SPREADS
Alert, planned inspection, repair, and restoration verified from readings
EXPECTED OUTCOMES
1
AI/ML platform for real-time FHTC monitoring
2
Early identification and prediction of disruptions, quality issues and failures
3
Community participation and service validation
4
Automatic integration with IMIS, Sujal Gaon IDs and JJM platforms
5
Preventive maintenance, transparency, evidence-based decisions
6
Reliable, accountable and sustainable FHTCs
ROADMAP
Idea submission
Working software platform
Bench rig with real nodes
Finale demo
Field pilot

## Slide 6: RESEARCH AND REFERENCES
Team Vistaar
Details / links of the reference and research work
[1] DDWS, Functionality Assessment of Household Tap Connection, National Report 2024
jaljeevanmission.gov.in/sites/default/files/2025-12/FHTC_Na...
[2] PIB, 13 Aug 2026: 75% of rural habitations covered with Sujal Gaon IDs
pib.gov.in/PressReleasePage.aspx?PRID=2298959
[3] PIB, 30 Dec 2025: Jal Seva Aankalan launched
pib.gov.in/PressReleasePage.aspx?PRID=2209798
[4] Cabinet, Mar 2026: JJM extended to Dec 2028, service-delivery focus
pmindia.gov.in/en/news_updates/
[5] JJM Dashboard (coverage, GIS, IoT pilot view)
ejalshakti.gov.in/JJMReport/JJMIndia.aspx
[6] JJM-WQMIS (laboratory and FTK water-quality testing)
ejalshakti.gov.in/WQMIS/
[7] PIB, 31 Mar 2021: JJM deploys sensor-based IoT devices (off-grid pilot)
pib.gov.in/PressReleaseIframePage.aspx?PRID=1708701
[8] Jal Jeevan Samvad, Oct 2023: IoT water-quality monitoring with complaint tracking
jaljeevanmission.gov.in/sites/default/files/2025-05/JalJeev...
[9] Systematic review: ML for anomaly detection in smart water metering networks (2024)
sciencedirect.com/science/article/pii/S1474706524000160
[10] SIH 2026 problem statement SIH26255, Ministry of Jal Shakti
sih.gov.in/sih2026PS
Working platform screens
Villager app: tap status and water quality (left); report a problem with photo and opt-in location (right)
Gram Panchayat: AI Early Warning with measured chlorine (top right) and Water Status with acoustic leak alerts (bottom right).
Demo video: [add YouTube link]
Source code: private repository, access on request (includes node firmware, gateway and an ESP32 simulation project)
pH, TDS and turbidity readings are screening indicators that trigger confirmatory laboratory or field-kit testing; they are not a safety certification.